## Slide 1
skyforce / RSEE4
2010/08/05
Color Engine SOP

## Slide 2: Why CCT?
為何要做CCT?
  面板原始色溫即非穩定不變
  色溫變化的原因
    R、G、 B不同灰階下光譜穿透率不一致
    Transmission Characteristic
      穿透率與波長具相關性，同樣電壓下不同波長穿透率皆不同
      LC Transmission formula
        u: 相位差
        Δn: 光程差, 隨液晶旋轉角度而改變
        d: cell gap (distance of ITO)
        λ: wavelength
        T: 穿透率
Chart: 
CIE Z
CIE X1
CIE X2
短波長區域
中波長區域
長波長區域
若波長與電壓無關， Nomalized的X、Y、Z應會重疊

## Slide 3: CCTv3 Improvement
Analyzer Mode Technique
  計算primary color weight wr wg wb
    XrYrZr、XgYgZg、XbYbZb
      the outputs when measuring target primary R will be Xr, Yr, Zr
      the outputs when measuring target primary G will be Xg, Yg, Zg
      the outputs when measuring target primary B will be Xb, Yb, Zb
    XYZmea
      respective x, y, z sensor outputs of measure color
    wr,wg,wb
      respective emission weighting for primary color R, G, B
    Primary Color以wr,wg,wb weighting組成XYZ mea
由XYZ mea推算wr,wg,wb weighting值

## Slide 4: CCTv3 Improvement
Analyzer Mode Technique
  計算target white intensity kr kg kb
    XrYrZr、XgYgZg、XbYbZb
      the outputs when measuring target primary R will be Xr, Yr, Zr
      the outputs when measuring target primary G will be Xg, Yg, Zg
      the outputs when measuring target primary B will be Xb, Yb, Zb
    XYZ tar
      respective x, y, z sensor outputs of target white color
    kr,kg,kb
      respective emission intensity for primary color R, G, B
      which comprise the adjustment standard target white color W will all be equal to 1 (= 100%).
計算target white的wr,wg,wb weighting值
    Intensity kr,kg,kb為相對於target white的weighting值